## Slide 1: F5 rSeries Learning with Alexander S

## Slide 2: Agenda 
  iSeries to rSeries
  F5OS Basic Setup
  F5OS Upgrade Procedure
  VLAN and LAG Configuration
    Configure VLANs
    Configure LAG (Link Aggregation Group)
    Assign VLANs to the LAG
  Tenant OS Deployment Preparation
  Tenant OS Deployment
  rSeries Tenant Basic Setup
  High Availability (HA) in rSeries Tenants
    Best Practices for rSeries Tenant HA
    rSeries Tenant HA Configuration

## Slide 3: Chapter 5 – Tenant OS deployment Preparation

## Slide 4: Chapter 5 – Tenant OS deployment Preparation 1. Tenant Names and Management IP Addresses

## Slide 5: Chapter 5 – Tenant OS deployment Preparation 2. Download and Import the tenant OS
Download and Import the tenant OS (Done this at chapter 3)
The tenant OS is now available on both rSeries hosts.
  TMOS Download

## Slide 6: Chapter 5 – Tenant OS deployment Preparation 3. Tenant Networking Layer – DATA LAG – Done this at Chapter 4
DATA LAG
  Assigned with vlan 230 for client side
  Assigned with vlan 231 for server side

## Slide 7: Chapter 5 – Tenant OS deployment Preparation 3. Tenant Networking Layer – HA LAG – Done this at Chapter 4
HA LAG
  Assigned with vlan 4001 for high availability

## Slide 8: Chapter 5 – Tenant OS deployment Preparation 4. Tenant MAC Block Size
🔍 Important Notes
The number of virtual servers you can configure is not directly limited by the MAC block size.
In standard routed mode deployments, multiple virtual servers can share the same MAC address assigned to the tenant’s interfaces.
How many unique MAC addresses are available for use within a tenant

## Slide 9: Chapter 5 – Tenant OS deployment Preparation 4. Tenant MAC Block Size – All the virtual servers uses interface MAC

## Slide 10: Chapter 5 – Tenant OS deployment Preparation 4. Tenant MAC Block Size – L2 inline mode need a unique MAC for each vs

## Slide 11: Chapter 5 – Tenant OS deployment Preparation 4. Tenant MAC Block Size – Always assign Large for production
Always choose Medium or Large MAC block sizes for production.
There is no negative impact or resource loss.
Larger MAC block provides more flexibility for scaling virtual servers.

## Slide 12: Chapter 5 – Tenant OS deployment Preparation 5. Resource Provisioning – Recommend / Advanced
Recommended
  DRAM allocation done by system based on vCPU selection.
  No flexibility to manually adjust DRAM allocation.

## Slide 13: Chapter 5 – Tenant OS deployment Preparation 5. Resource Provisioning – Recommend / Advanced
Advanced
  Provides the option to manually configure both vCPUs and DRAM, allowing customization beyond the default recommendations.

## Slide 14: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
Configured
Provisioned
Deployed
Tenant’s settings and parameters are defined and saved in the F5OS
System resources such as vCPU, memory, and disk space are allocated to the tenant.
The tenant is active and running. It is utilizing the allocated CPU, memory, and virtual disk to perform its intended functions.
Settings & Parameters
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Only for the initial deployment
No resources allocated

## Slide 15: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
Configured
(Initial deployment)
Settings & Parameters
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Provisioned
Deployed
Don’t change provisioned to configured
Don’t change deployed to configured
Stop the tenant
Delete the tenant’s virtual disk
(Delete the BIGIP configuration)
Release system resources.
Release system resources.
(Reset the configuration and run time status!!)

## Slide 16: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
Configured
Provisioned
Deployed
Tenant’s settings and parameters are defined and saved in the F5OS
System resources such as vCPU, memory, and disk space are allocated to the tenant.
The tenant is active and running. It is utilizing the allocated CPU, memory, and virtual disk to perform its intended functions.
Settings & Parameters
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Only for the initial deployment
No resources allocated
Tenant is not active!

## Slide 17: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Provisioned
Deployed
Gracefully shut down the running tenant.
Preserve the virtual disk and all configuration data.
During the host upgrade
Allowing the tenant to be restarted later without reconfiguration

## Slide 18: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
Configured
Provisioned
Deployed
Tenant’s settings and parameters are defined and saved in the F5OS
System resources such as vCPU, memory, and disk space are allocated to the tenant.
The tenant is active and running. It is utilizing the allocated CPU, memory, and virtual disk to perform its intended functions.
Settings & Parameters
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Only for the initial deployment
No resources allocated
Tenant is not active!

## Slide 19: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Provisioned
Deployed
Configured
(Initial deployment)
Settings & Parameters
Resources are allocated and the tenant starts
The tenant starts using already-allocated resources.

## Slide 20: Chapter 5 – Tenant OS deployment Preparation 7. Enabling Crypto Acceleration
Improves Cryptographic Speed and Efficiency on F5 rSeries
CPU handles general traffic processing
CPU offloads SSL/TLS decryption encryption to Crypto Acceleration Module.
Traffic Flow:
  Encrypted traffic enters the appliance
  SSL/TLS is offloaded to the crypto module
  Decrypted traffic is returned to the CPU for further processing
  Clean traffic exits to internal services
  Must enable Crypto Acceleration

## Slide 21: Chapter 5 – Tenant OS deployment Preparation 8. Appliance mode
Appliance mode
Tenant is designed to perform a specific task. For example this tenant does the WAF protection.
Key - Dedicated resources assigned to that tenant regardless of the usage.
Non Appliance Mode
Tenant is designed to perform more tasks like LTM, ASM and APM.
Key - Shared resources assigned to the tenant.
WAF
(Resource dedicated)
ADC – LTM+WAF+APM
(Resource shared between the modules)

## Slide 22: Please continue by watching the next video. Next video is – Tenant OS Deployment – Thank you!!!